## Slide 1: LAN Switching and VLAN

## Slide 2: Table of Contents
Switching
The Spanning-Tree Protocol
VLAN
  Introduction of VLAN
  VLAN Architecture
  VLAN Implementation
  Routing Between VLANs

## Slide 3: Switch Operation
Switches perform two basic functions:
  Building and maintaining switching tables (similar to a bridge table) based on MAC addresses
  Switching frames out the interface to the destination

## Slide 4: Symmetric Switching
  symmetric switching provides switched connections between ports with the same bandwidth (10/10 Mbps or 100/100 Mbps)
  can cause bottlenecks as users try to access servers on other segments.
potential bottlenecks
Notes: Cisco catalyst 都是非对称的

## Slide 5: Asymmetric Switching
  asymmetric switching reduces the likelihood of a potential bottleneck at the server by attaching the segment with the server to a higher bandwidth port (100 Mbps)
  asymmetric switching requires memory buffering in the switch

## Slide 6: Memory Buffering
Area of memory in a switch where destination and transmission data are stored until it can be switched out the correct port.
  Port-based memory buffering
    packets are stored in a queue on each port
    possible for one packet to delay transmission of other packets because of a busy destination port
  Shared memory buffering
    common memory buffering shared by all ports
    allows packets to be RX on one port and TX out another port without changing it to a different queue.
Notes:   Port-based memory buffering可能会由于目的端口堵塞而导致源端口的帧不得转发而耽误源端口后面的帧不得正常发送。
  Shared memory buffering动态分配各个端口所需要的缓存内存量

## Slide 7: Switching Methods
Store-and-Forward
  The switch receives the entire frame, calculating the CRC at the end, before sending it to the destination
Cut-through
  A switch adds latency. It can be reduced by using cut-through switching method
  Fast forward switching--only checks the destination MAC before immediately forwarding the frame
  Fragment Free--reads the first 64 bytes to reduce errors before forwarding the frame

## Slide 8: Two Switching Methods

## Slide 9: Layer 2 Switching
Notes: 二层交换机：一个mac 三层交换机：一个端口一个mac 路由器：一个以太网口一个mac，桥接口、串行口没有mac

## Slide 10: Layer 3 Switching

## Slide 11: Layer 4 Switching

## Slide 12: Multilayer Switching

## Slide 13: Table of Contents
Switching
The Spanning-Tree Protocol
VLAN
  Introduction of VLAN
  VLAN Architecture
  VLAN Implementation
  Routing Between VLANs

## Slide 14: Bridging Loops
  Loops may occur in a network for a variety of reasons.
    Usually loops in networks are the result of a deliberate attempt to provide redundancy.
    Can also occur by configuration error
      Two primary reasons loops can be absolutely disastrous in a bridged network:
        broadcast loops
        bridge-table corruption

## Slide 15: Redundancy Creates Loops

## Slide 16: L2 Loops
Broadcasts and Layer 2 loops can be a dangerous combination.
Ethernet frames have no TTL field
After an Ethernet frame starts to loop, it will probably continue until someone shuts off one of the switches or breaks a link
The switches will flip flop the bridging table entry for Host A (creating extremely high CPU utilization).

## Slide 17: L2 Loops - Flooded unicast frames
Where’s Host B? FLOOD
Where’s Host B? FLOOD
Where’s Host B? FLOOD
Where’s Host B? FLOOD
Uh oh.
Removed from the network
And the floods continue

## Slide 18: Overview of STP
Elements of the Spanning Tree Protocol
  Main function: allow redundant paths in a switched/bridged network without incurring latency from the effects of loops.
  STP prevents loops by calculating a stable spanning-tree network topology
  Spanning-tree frames (called bridge protocol data units--BPDUs) are used to determine the spanning-tree topology

## Slide 19: STP Decision Sequence
  Spanning Tree always uses the same four-step decision sequence:
    Lowest root BID (Bridge Identification)
    Lowest path cost to root bridge
    Lowest sender BID
    Lowest port ID

## Slide 20: BPDUs
BPDUs are switch-to-switch traffic; they do not carry end-user traffic.
STP establishes a root node, called the root bridge
The resulting tree originates from the root bridge.
Redundant links that are not part of the shortest path tree are blocked.
Data frames received on blocked links are dropped.
The message that a switch sends, allowing the formation of a loop free logical topology, is BPDU

## Slide 21: STP BPDU

## Slide 22: Bridge Identification/BID
A Bridge ID (BID): 8 bytes
  The high-order BID subfield(2 bytes): bridge priority
    216 possible values: 0-65,535 (default: 32,768)
    Typically expressed in a decimal format
  The low-order subfield(6 bytes): a MAC address assigned to the switch
    Expressed in hexadecimal format
STP cost values: lower costs are better.

## Slide 23: Electing the Root Switch
  The switches elect a single root switch by looking for the switch with the lowest BID (often referred to as a root war).
  If all the switches are using the default bridge priority of 32,768, the lowest MAC address serves as the tie-breaker.

## Slide 24: Path Cost
Bridges use the concept of cost to evaluate how close they are to other bridges.

## Slide 25: Five STP States
  States are established by configuring each port according to policy
  Then the STP modifies the states based on traffic patterns and potential loops
  The default order of STP states are:
    Blocking--no frames forwarded, BPDUs heard
    Listening--no frames forwarded, listening for data frames
    Learning--no frames forwarded, learning addresses
    Forwarding--frames forwarded, learning addresses
    Disabled--no frames forwarded, no BPDUs heard
blocking
forwarding
20s
15s
15s

## Slide 26: Initial STP Convergence
  When the network first starts, all the bridges flood the network with a mix of BPDU information.
  Immediately, they apply the decision sequence allowing them to hone in on the set of BPDUs that form a single spanning tree for the entire network.
(Step 1) Root switch decision: A single root bridge is elected to act as the central point of this network
(Step 2) Electing the root ports: All the remaining bridges calculate a set of root ports
(Step 3) Electing the designated ports: All the remaining bridges calculate a set of designated ports
Notes: Hone：磨练

## Slide 27: Step1: Root Switch Decision
Announce itself as the root
Checking all BPDUs received on the port as well as the BPDU that would be sent on that port
For each arrived BPDU, if it is lower in value than the existing BPDU saved for the port
  The old value is replaced
  The sender of BPDU is accepted as the new root
Root

## Slide 28: Step2: Electing the Root Ports
Every non-root bridge must select one root port.
  The root port of a bridge is the port that is closest to the root bridge.
  The root path cost is the cumulative cost of all links to the root bridge.
STP costs are incremented as BPDUs are received on a port, not as they are sent out a port.
Notes: ROOT port选择时可能要比较端口号，可以配置交换机各个端口的优先级。默认是128

## Slide 29: Step3: Electing Designated Ports(I)
Each segment has one designated port
  Functions as the single bridge /switch port that both sends and receives traffic to and from that segment and the root bridge.
The bridge/switch containing the designated port for a given segment is referred to as the designated bridge for that segment.
All the bridges/switches will block the non-designated ports on them
Every active port on the root bridge becomes a designated port

## Slide 30: Step3: Electing Designated Ports(II)
Blocked
Notes: 比较BID

## Slide 31: An Example of STP
Root switch
Designated port
Designated port
Root port
Root port
Non-designated port
Blocked
100BaseT
10BaseT
MAC: 0c00c8111111
Priority: 32768
MAC: 0c00c8211112
Priority: 32768
MAC: 0c00c8111110
Priority: 32768
Designated port

## Slide 32: Table of Contents
Switching
The Spanning-Tree Protocol
VLAN
  Introduction of VLAN
  VLAN Architecture
  VLAN Implementation
  Routing Between VLANs

## Slide 33: Existing Shared LAN Configurations
In a typical shared LAN...
  Users are grouped physically based on the hub they are plugged into
  Routers segment the LAN and provide broadcast firewalls
In VLANs...
  you can group users logically by function, department or application in use
  configuration is done through proprietary software

## Slide 34: Differences between LANs & VLANs
VLANs...
  work at Layer 2 & 3
  control network broadcasts
  allow users to be assigned by net admin.
  provide tighter network security. How?
Notes: 安全
成本降低
性能提高
广播风暴防范
提高IT员工的效率
简化项目管理或应用管理

## Slide 35: VLANs (IEEE 802.1q)
Characteristics
  A logical grouping of network devices or users that are not restricted to a physical switch segment.
  The devices or users in a VLAN can be grouped by function, department, application, and so on, regardless of their physical segment location.
  A VLAN creates a single broadcast domain that is not restricted to a physical segment and is treated like a subnet.
  VLAN setup is done in the switch by the network administrator using the vendor’s software.

## Slide 36: Grouping Users
  VLANs can logically segment users into different subnets (broadcast domains)
  Broadcast frames are only switched between ports on the switch or switches with the same VLAN ID.
  Users can be logically group via software based on:
    port number
    MAC address
    protocol being used
    application being used

## Slide 37: Table of Contents
Switching
The Spanning-Tree Protocol
VLAN
  Introduction of VLAN
  VLAN Architecture
  VLAN Implementation
  Routing Between VLANs

## Slide 38: VLANs Across the Backbone
  VLAN configuration needs to support backbone transport of data between interconnected routers and switches.
  The backbone is the area used for inter-VLAN communication
  The backbone should be high-speed links, typically 100Mbps or greater

## Slide 39: Router’s Role in a VLAN
A router provides connection between different VLANs
For example, you have VLAN1 and VLAN2.
  Within the switch, users on separate VLANs cannot talk to each other (benefit of a VLAN!)
  However, users on VLAN1 can email users on VLAN2 but they need a router to do it.

## Slide 40: How Frames are Used in a VLAN
Switches make filtering and forwarding decisions based on data in the frame.
There are two techniques used.
  Frame Filtering--examines particular information about each frame (MAC address or layer 3 protocol type)
  Frame Tagging--places a unique identifier in the header of each frame as it is forwarded throughout the network backbone.

## Slide 41: Frame Filtering

## Slide 42: Frame Tagging
Frame tagging implementation process:
  Places a VLAN identifier in the header of each frame as it is forwarded throughout the network backbone.
  The identifier is understood and examined by each switch.
  When the frame exits the network backbone, the switch removes the identifier before the frame is transmitted to the target end station.
Frame tagging functions at Layer 2 and requires little processing or administrative overhead.

## Slide 43: Frame Tagging

## Slide 44: Frame Tagging– IEEE802.1Q and ISL
IEEE802.1Q
  IEEE Standard, insert a label of VLAN to the header to identify the VLAN belonging to. (Frame Tagging)。
ISL(Inter-Switch Link)
  Cisco proprietary. ISL add a header of 26 bytes in front of the data frame, and appends a CRC(4 byte) at the end.
Name | Encapsulation | Label | Media
802.1Q | No | Yes | Ethernet
ISL | Yes | No | Ethernet

## Slide 45: Table of Contents
Switching
The Spanning-Tree Protocol
VLAN
  Introduction of VLAN
  VLAN Architecture
  VLAN Implementation
  Routing Between VLANs

## Slide 46: Ports, VLANs, and Broadcasts
Methods for implementing VLANs
  Static
  Dynamic
Each switched port can be assigned to a VLAN. This...
  ensures ports that do not share the same VLAN do not share broadcasts.
  ensures ports that do share the same VLAN will share broadcasts.

## Slide 47: Static VLANs

## Slide 48: Static VLANs
Defined
  Static VLANs are when ports on a switch are administratively assigned to a VLAN
Benefits
  secure, easy to configure and monitor
  works well in networks where moves are controlled

## Slide 49: Dynamic VLANs

## Slide 50: Dynamic VLANs
  When a station is initially connected to an unassigned port, the switch checks an entry in the table and dynamically configures the port with the right VLAN
  Benefits
    less administration (more upfront) when users are added or move
    centralized notification of unauthorized user
Notes: Upfront:前期

## Slide 51: Port-Centric VLANs
3 Port-Centric VLANs

## Slide 52: Benefits of Port-Centric VLANs
  All nodes in the same VLAN are attached to the same router interface
  Makes management easier because...
    Users are assigned by router port
    VLANs are easy to admin.
    provides increased security
    packets do not “leak” into other domains

## Slide 53: Access and Trunk Links

## Slide 54: Access Links
An access link is a link on the switch that is a member of only one VLAN.
This VLAN is referred to as the native VLAN of the port.
  Any device that is attached to the port is completely unaware that a VLAN exists.

## Slide 55: Trunk Links
A trunk link is capable of supporting multiple VLANs.
Trunk links are typically used to connect switches to other switches or routers.
Switches support trunk links on both Fast Ethernet and Gigabit Ethernet ports.
Access and trunk links exist, too

## Slide 56: Trunk Links
Without trunking
With trunking
A trunk is a point-to-point link that supports several VLANs
A trunk is to saves ports when creating a link between two devices implementing VLANs

## Slide 57: Trunk Links
A trunk link does not belong to a specific VLAN.
  Acts as a conduit for VLANs between switches and routers.
The trunk link can be configured to transport all VLANs or to transport a limited number of VLANs.
A trunk link may, however, have a native VLAN.
  The native VLAN of the trunk is the VLAN that the trunk uses if the trunk link fails for any reason.

## Slide 58: Configuration in Switch 29xx
The following guidelines must be followed when configuring VLANs on Cisco 29xx switches:
The maximum number of VLANs is switch dependent.
VLAN 1 is one of the factory-default VLANs.
VLAN 1 is the default Ethernet VLAN.
Cisco Discovery Protocol (CDP) and VLAN Trunking Protocol (VTP) advertisements are sent on VLAN 1.
The Catalyst 29xx IP address is in the VLAN 1 broadcast domain by default.

## Slide 59: VLAN Configuration
Step1: The steps necessary to create the VLAN. A VLAN name may also be configured, if necessary.
Switch# vlan database Switch(vlan)# vlan vlan_number Switch(vlan)# exit
Step2: Assign the VLAN to one or more interfaces:
Switch(config)# interface fastethernet 0/9 Switch(config-if)# switchport access vlan vlan_number

## Slide 60: Adding a VLAN Example
cat2950#vlan database
cat2950(vlan)#vlan 9 name switchlab90
VLAN 9 added:
Name: switchlab90
cat2950(vlan)#?
VLAN database editing buffer manipulation commands:
abort Exit mode without applying the changes
apply Apply current changes and bump revision number
exit Apply changes, bump revision number, and exit mode
reset Abandon current changes and reread current database
cat2950(config)#interface fa 0/2
cat2950(config-if)# switchport access vlan 9

## Slide 61: Verifying a VLAN
cat2950#sh vlan
VLAN Name Status Ports
---- ------------------------ ------------ ------------
Default active Fa0/1, Fa0/3
9 switchlab90 active Fa0/2
1002 fddi-default active
1003 token-ring-default active
1004 fddinet-default active
1005 trnet-default active
Switch# show vlan [vlanid]
Notes: Layer 1 of 2

## Slide 62: Deleting VLANs
cat2950(vlan)#no vlan 9
Deleting VLAN 9...
cat2950(vlan)#exit
APPLY completed.
Exiting....
cat2950#
When a VLAN is deleted any ports assigned to that VLAN become inactive. The ports will, however, remain associated with the deleted VLAN until assigned to a new VLAN.
switch(vlan)# no vlan vlanid [name vlan-name]

## Slide 63: Table of Contents
Switching
The Spanning-Tree Protocol
VLAN
  Introduction of VLAN
  VLAN Architecture
  VLAN Implementation
  Routing Between VLANs

## Slide 64: Routing Between VLANs

## Slide 65: Routing Between VLANs

## Slide 66: Subinterfaces

## Slide 67: Configuring Inter-VLAN Routing
Step3: Assign an IP address to the interface
Step1: Identify the interface.
Router(config)#interface fastethernet port-number. subinterface-number
Step2: Define the VLAN encapsulation.
Router(config-if)#encapsulation dot1q vlan-number
Router(config-if)#ip address ip-address subnet-mask

## Slide 68: Configuring Inter-VLAN Routing
Sydney(config)#interface FastEthernet 0/0
Sydney(config-if)#full duplex
Sydney(config-if)#no shut
Sydney(config-if)#interface FastEthernet 0/0.1
Sydney(config-subif)#encapsulation 802.1q 1
Sydney(config-subif)#ip address 192.168.1.1 255.255.255.0
Sydney(config-if)#interface FastEthernet 0/0.2
Sydney(config-subif)#encapsulation 802.1q 20
Sydney(config-subif)#ip address 192.168.2.1 255.255.255.0
Sydney(config-if)#interface FastEthernet 0/0.3
Sydney(config-subif)#encapsulation 802.1q 30
Sydney(config-subif)#ip address 192.168.3.1 255.255.255.0

## Slide 69
谢 谢！