## Slide 1: Network Security

## Slide 2: Network Security
网络安全问题概述
一般的数据加密模型
对称密钥和公钥密码体制
数字签名
防火墙
  访问控制列表ACL

## Slide 3: 网络安全问题概述
计算机网络上的通信面临以下的四种威胁：
(1) 截获——从网络上窃听他人的通信内容。
(2) 中断——有意中断他人在网络上的通信。
(3) 篡改——故意篡改网络上传送的报文。
(4) 伪造——伪造信息在网络上传送。

## Slide 4: 被动攻击和主动攻击
截获
篡改
伪造
中断
被动攻击
主 动 攻 击
目的站
源站
源站
源站
源站
目的站
目的站
目的站
截获信息的攻击称为被动攻击
更改信息和拒绝用户使用资源的攻击称为主动攻击。

## Slide 5: 被动攻击和主动攻击
在被动攻击中，攻击者只是观察和分析某一个协议数据单元 PDU 而不干扰信息流。
主动攻击是指攻击者对某个连接中通过的 PDU 进行各种处理。
  更改报文流
  拒绝报文服务
  伪造连接初始化

## Slide 6: 计算机网络通信安全的目标
防止析出报文内容
防止通信量分析
检测更改报文流
检测拒绝报文服务
检测伪造初始化连接

## Slide 7: 恶意程序(malicious program)
计算机病毒——会“传染”其他程序的程序，“传染”通过修改其他程序来把自身或其变种复制进去而完成。
计算机蠕虫——通过网络的通信功能将自身从一个结点发送到另一个结点并启动运行的程序。
特洛伊木马——一种程序，它执行的功能超出所声称的功能。
逻辑炸弹——一种当运行环境满足某种特定条件时执行其他特殊功能的程序。

## Slide 8: 计算机网络安全的内容
保密性
安全协议的设计
访问控制

## Slide 9: Network Security
网络安全问题概述
一般的数据加密模型
对称密钥和公钥密码体制
数字签名
防火墙
  访问控制列表ACL

## Slide 10: 一般的数据加密模型
明文 X
截获
密文 Y
加密密钥 K
明文 X
密文 Y
截取者
篡改
A
B
E 运算
加密算法
D 运算
解密算法
因特网
解密密钥 K

## Slide 11: 一些重要概念
密码编码学(cryptography)是密码体制的设计学，而密码分析学(cryptanalysis)则是在未知密钥的情况下从密文推演出明文或密钥的技术。密码编码学与密码分析学合起来即为密码学(cryptology)。
如果不论截取者获得了多少密文，但在密文中都没有足够的信息来唯一地确定出对应的明文，则这一密码体制称为无条件安全的，或称为理论上是不可破的。
如果密码体制中的密码不能被可使用的计算资源破译，则这一密码体制称为在计算上是安全的。

## Slide 12: Network Security
网络安全问题概述
一般的数据加密模型
对称密钥和公钥密码体制
数字签名
防火墙
  访问控制列表ACL

## Slide 13: 对称密钥密码体制
所谓常规密钥密码体制，即加密密钥与解密密钥是相同的密码体制。
这种加密系统又称为对称密钥系统。
对称加密算法 | 密钥长度 (按位) | 描述
DES | 56 | 1970年代由IBM公司设计，直到1997年之前是作为NIST 标准。 尽管思想已经过时，但DES仍在广泛使用。 设计时仅仅考虑在硬件上执行，因此在软件上运行速度很慢。
3DES | 112 和 168 | 基于连续三次使用DES的技术意味着输入数据被进行了三次加密，因此被认为是远强于DES。 但是，相比于一些新的分组加密算法，它仍然很慢，比如AES。
AES | 128, 192, 和 256 | 软件和硬件运行都很快，相对易于实施，内存要求低。 作为一种新的加密标准，正被大规模地采用。
软件加密算法—Software Encryption Algorithm (SEAL) | 160 | SEAL 是DES、3DES和AES的一种替代算法。它使用160位加密密钥，与其他基于软件的算法相比较，对CPU的影响更小。
RC 系列算法 | RC2 (40 和 64) RC4 (1 至 256) RC5 (0至 2040) RC6 (128, 192, 和 256) | 由Ron Rivest 发明设计的一套对称密钥加密算法。 RC1 没有公布， RC3在没有正式使用前就废除了。 RC4 是世界上最为广泛使用的流密码。 RC6, 是基于RC5的128位分组加密，是1997年AES最有力的竞争对手（最终Rijndael胜出）。

## Slide 14: 数据加密标准 DES
数据加密标准 DES 属于常规密钥密码体制，是一种分组密码。
在加密前，先对整个明文进行分组。每一个组长为 64 位。
然后对每一个 64 位 二进制数据进行加密处理，产生一组 64 位密文数据。
最后将各组密文串接起来，即得出整个的密文。
使用的密钥为 64 位（实际密钥长度为 56 位，有 8 位用于奇偶校验)。

## Slide 15: DES 的保密性
DES 的保密性仅取决于对密钥的保密，而算法是公开的。尽管人们在破译 DES 方面取得了许多进展，但至今仍未能找到比穷举搜索密钥更有效的方法。
DES 是世界上第一个公认的实用密码算法标准，它曾对密码学的发展做出了重大贡献。
目前较为严重的问题是 DES 的密钥的长度。
现在已经设计出来搜索 DES 密钥的专用芯片。

## Slide 16: 公钥密码体制
公钥密码体制使用不同的加密密钥与解密密钥，是一种“由已知加密密钥推导出解密密钥在计算上是不可行的”密码体制。
公钥密码体制的产生主要是因为两个方面的原因，一是由于常规密钥密码体制的密钥分配问题，另一是由于对数字签名的需求。
现有最著名的公钥密码体制是RSA 体制，它基于数论中大数分解问题的体制，由美国三位科学家 Rivest, Shamir 和 Adleman 于 1976 年提出并在 1978 年正式发表。
 | 密钥长度 (按位) | 描述
DH | 512, 1024, 2048 | 1976年由Whitfield Diffie 和 Martin Hellman发明。 双方协商得到同一个密钥来加密消息。 基于这样的假定：给定幂指数和底数，很容易得到乘方值，但给定乘方结果和底数，要计算幂指数是很困难的。
数字签名标准 (DSS) 和数字签名算法 (DSA) | 512 - 1024 | 由 NIST创建并把DSA作为数字签名的算法。 是一种基于ElGama签名方案的公钥算法。 和RSA相比，签名创建的速度差不多，但校验时就慢得多。
RSA 加密算法 | 512 到 2048 | 1977年由 Ron Rivest, Adi Shamir和 Leonard Adleman 在 麻省理工学院（MIT） 基于当前大数因式分解计算困难的数学难题 既适合加密有适合签名 广泛用于电子商务协议
EIGamal | 512 - 1024 | 基于Diffie-Hellman 密钥协商. 由Taher Elgamal于1984年发明并用在GNU Privacy Guard （一个加密程序）软件、PGP和其他加密系统上。 加密后的信息是源信息的两倍长，因此适合用于较短信息的加密，例如对密钥加密。
椭圆曲线技术 | 160 | 由 Neil Koblitz在1987年发明，而Victor Miller则在1986年发明。 能被许多加密算法采用 密钥可以非常短

## Slide 17: 公钥密码体制
密文Y
E 运算
加密算法
D 运算
解密算法
加密
解密
明文 X
明文 X
A
B
B 的私钥 SKB
密文Y
因特网
B 的公钥 PKB
在公钥密码体制中，加密密钥(即公钥) PK 是公开信息，而解密密钥(即私钥或秘钥) SK 是需要保密的
加密算法 E 和解密算法 D 也都是公开的
虽然SK 是由PK 决定的，但却不能根据 PK 计算出 SK

## Slide 18: 公钥算法的特点
发送者 A 用 B 的公钥 PKB 对明文 X 加密（E 运算）后，在接收者 B 用自己的私钥 SKB 解密（D 运算），即可恢复出明文：
解密密钥是接收者专用的秘钥，对其他人都保密。
加密密钥是公开的，但不能用它来解密，即

## Slide 19: 公钥算法的特点（续）
加密和解密的运算可以对调，即
在计算机上可容易地产生成对的 PK 和 SK。
从已知的 PK 实际上不可能推导出 SK，即从 PK 到 SK 是“计算上不可能的”。
加密和解密算法都是公开的。

## Slide 20: 应当注意
任何加密方法的安全性取决于密钥的长度，以及攻破密文所需的计算量
在这方面，公钥密码体制并不比传统加密体制更加优越
由于目前公钥加密算法的开销较大，在可见的将来还不会放弃传统的加密方法
公钥需要密钥分配协议，具体的分配过程并不比采用传统加密方法时更简单

## Slide 21: Network Security
网络安全问题概述
一般的数据加密模型
对称密钥和公钥密码体制
数字签名
防火墙
  访问控制列表ACL

## Slide 22: 数字签名
数字签名必须保证以下三点：
  报文鉴别——接收者能够核实发送者对报文的签名
  报文的完整性——发送者事后不能抵赖对报文的签名
  不可否认——接收者不能伪造对报文的签名
现在已有多种实现各种数字签名的方法。但采用公钥算法更容易实现

## Slide 23: 数字签名的实现
密文
D
运算
明文 X
明文 X
A
B
A 的私钥 SKA
因特网
签名
核实签名
E
运算
密文
A 的公钥 PKA

## Slide 24: 数字签名的实现
因为除 A 外没有别人能具有 A 的私钥，所以除 A 外没有别人能产生这个密文。因此 B 相信报文 X 是 A 签名发送的。
若 A 要抵赖曾发送报文给 B，B 可将明文和对应的密文出示给第三者。第三者很容易用 A 的公钥去证实 A 确实发送 X 给 B。
反之，若 B 将 X 伪造成 X‘，则 B 不能在第三者前出示对应的密文。这样就证明了 B 伪造了报文。

## Slide 25: 具有保密性的数字签名
核实签名
解密
加密
签名
E 运算
D 运算
明文 X
明文 X
A
B
A 的私钥 SKA
因特网
E 运算
B 的私钥 SKB
D 运算
加密与解密
签名与核实签名
B 的公钥 PKB
A 的公钥 PKA
密文

## Slide 26: Network Security
网络安全问题概述
一般的数据加密模型
对称密钥和公钥密码体制
数字签名
防火墙
  访问控制列表ACL

## Slide 27: 防火墙(firewall)
防火墙是由软件、硬件构成的系统，是一种特殊编程的路由器，用来在两个网络之间实施接入控制策略。接入控制策略是由使用防火墙的单位自行制订的，为的是可以最适合本单位的需要。
防火墙内的网络称为“可信赖的网络”(trusted network)，而将外部的因特网称为“不可信赖的网络”(untrusted network)。
防火墙可用来解决内联网和外联网的安全问题。

## Slide 28: 防火墙在互连网络中的位置
G
内联网
可信赖的网络
不可信赖的网络
分组过滤
路由器 R
分组过滤
路由器 R
应用网关
外局域网
内局域网
防火墙
因特网

## Slide 29: 防火墙的功能
防火墙的功能有两个：阻止和允许。
“阻止”就是阻止某种类型的通信量通过防火墙（从外部网络到内部网络，或反过来）。
“允许”的功能与“阻止”恰好相反。
防火墙必须能够识别通信量的各种类型。不过在大多数情况下防火墙的主要功能是“阻止”。

## Slide 30: 防火墙技术一般分为两类
网络级防火墙——用来防止整个网络出现外来非法的入侵。属于这类的有分组过滤和授权服务器
  前者检查所有流入本网络的信息，然后拒绝不符合事先制订好的一套准则的数据
  后者则检查用户的登录是否合法
应用级防火墙——从应用程序来进行接入控制。通常使用应用网关或代理服务器来区分各种应用
  例如，可以只允许通过访问万维网的应用，而阻止 FTP 应用通过

## Slide 31: What Are ACLs?
  An ACL is a list of instructions that tells a router what type of packets to permit or deny.
    You must configure an ACL if you want a router to deny some packets. Otherwise, the router will accept and forward all packets as long as the link is up.
    You can permit or deny packets based upon such thing as:
      Source address
      Destination address
      Upper Layer protocols (e.g. TCP & UDP ports)

## Slide 32: Testing Packets with ACLs
  To determine whether a packet is to be permitted or denied, it is tested against the ACL statements in sequential order.
    When a statement “matches,” no more statements are evaluated.
    The packet is either permitted or denied.
  There is an implicit “deny any” statement at the end of the ACL
    If a packet does not match any of the statements in the ACL, it is dropped.

## Slide 33: Testing Packets with ACLs
Example:
  If we have an ACL list described as below:
    1. Permit packets from 192.168.100.1 to pass
    2. Permit packets from 192.168.100.2 to pass
    3. Deny packets from 192.168.100.3
  Then:
    Packets from 192.168.100.1 will be forwarded
    Packets from 192.168.100.3 will be denied
    But how does the router process the packets from 192.168.100.4?
      Packets from 192.168.100.4 will be denied

## Slide 34: How a Router Uses an ACL (outbound)
  Check to see if packet is routable. If so, look up route in routing table
  Check for an ACL for the outbound interface
    If no ACL, switch the packet out the destination interface
    If an ACL, check the packet against the ACL statements sequentially--denying or permitting based on a matched condition.
  If no statement matches, what happens?
      Deny all these packets!

## Slide 35: Outbound Standard ACL Process
Outgoing Packet
Do route table lookup
ACL on interface?
Does source address match?
Next entry in list
More entries?
Apply condition
Permit
Deny
No
No
No
Yes
Yes
Yes
ICMP Message
Forward Packet

## Slide 36: Two Basic Tasks (Standard ACL)
Write the ACL statements sequentially in global configuration mode.
  Router(config)#access-list access-list-number {permit/deny} {test-conditions}
  Lab-D(config)#access-list 1 deny 192.5.5.10 0.0.0.0
Group the ACL to one or more interfaces in interface configuration mode.
  Router(config-if)#{protocol} access-group access-list-number {in/out}
  Lab-D(config-if)#ip access-group 1 out

## Slide 37: The access-list-number parameter
ACLs come in many types. The access-list-number specifies what types.
The table below shows common access list types.
ACL Type | ACL Number
IP Standard | 1 to 99
IP Extended | 100 to 199
AppleTalk | 600 to 699
IPX Standard | 800 to 899
IPX Extended | 900 to 999
IPX SAP | 1000 to 1099
Router(config)#access-list access-list-number {permit/deny}{test-conditions}

## Slide 38: The permit/deny parameter
  After you’ve typed access-list and chosen the correct access-list-number, you type either permit or deny depending on the action you wish to take.
Permit
Deny
ICMP Message
Forward Packet
Router(config)#access-list access-list-number {permit/deny}{test-conditions}

## Slide 39: The {test-conditions} parameter
In the {test conditions} portion of the ACL, common to most access lists is the source address’ ip mask and wildcard mask.
The source address can be a subnet, a range of addresses, or a single host. It is also referred to as the ip mask because the wildcard mask uses the source address to check bits.
The wildcard mask tells the router what bits to check.
Router(config)#access-list access-list-number {permit/deny}{test-conditions}
Lab-A(config)#access-list 1 deny 192.5.5.10 0.0.0.0
ip mask
wildcard
mask

## Slide 40: The Wildcard Mask
A wildcard mask is written to tell the router what bits in the address to match and what bits to ignore.
  A “0” bit means check this bit position
  A “1” means ignore this bit position
Our previous example of 192.5.5.10 0.0.0.0 can be rewritten in binary as:
  11000000.00000101.00000101.00001010 (Source address)
  00000000.00000000.00000000.00000000 (Wildcard mask)

## Slide 41: Masking Practice
Write an ip mask and wildcard mask to check for all hosts on the network: 192.5.5.0 255.255.255.0
Answer: 192.5.5.0 0.0.0.255
  Notice that this wildcard mask is a mirror image of the default subnet mask for a Class C address.
  WARNING: This is a helpful rule only when looking at whole networks or subnets.

## Slide 42: Masking Practice
Write an ip mask and wildcard mask to check for all hosts in the subnet: 192.5.5.32 255.255.255.224
  If you answered 192.5.5.32 0.0.0.31 YOU’RE RIGHT!!
  0.0.0.31 is the mirror image of 255.255.255.224
  Let’s look at both in binary:
    11111111.11111111.11111111.11100000 (255.255.255.224)
    00000000.00000000.00000000.00011111 (0.0.0.31)

## Slide 43: Time Savers: the any command
  Since ACLs have an implicit “deny any” statement at the end, you must write statements to permit others through.
  Using our previous example, if the students are denied access and all others are allowed, you would write two statements:
    Lab-A(config)#access-list 1 deny 192.5.5.0 0.0.0.127
    Lab-A(config)#access-list 1 permit 0.0.0.0 255.255.255.255
  Since the last statement is commonly used to override the “deny any,” Cisco gives you an option--the any command:
    Lab-A(config)#access-list 1 permit any

## Slide 44: Time Savers: the host command
Many times, a network administrator will need to write an ACL to permit a particular host (or deny a host). The statement can be written in two ways. Either...
  Lab-A(config)#access-list 1 permit 192.5.5.10 0.0.0.0
or...
  Lab-A(config)#access-list 1 permit host 192.5.5.10

## Slide 45: Correct Placement of Standard ACLs
  Standard ACLs do not have a destination parameter. Therefore, you place standard ACLs as close to the destination as possible.
  To see why, ask yourself what would happen to all ip traffic if you placed a “deny 192.5.5.0 0.0.0.255” statement on Lab-A’s E0?

## Slide 46: Correct Placement of Standard ACLs

## Slide 47: Extended ACL Overview
Extended ACLs are numbered from 100 - 199 and “extend” the capabilities of the standard ACL.
Extensions include the ability to filter traffic based on...
  destination address
  portions of the ip protocol
    You can write statements to deny only protocols such as “icmp” or routing protocols like “rip” and “igrp”
  upper layers of the TCP/IP protocol suite
    You can write statements to deny only protocols such as “tftp” or “http”
    You can use an operand like eq, gt, lt, and neq (equal to, greater than, less than, and not equal to) to specify how to handle a particular protocol.
    For example, if you wanted an access list to permit all traffic except http access, you would use permit ip any any neq 80

## Slide 48: Two Basic Tasks (Extended ACL)
  Write the ACL statements sequentially in global configuration mode.
    Router(config)# access-list access-list-number {permit|deny} {protocol|protocol-keyword}{source source-wildcard} {destination destination-wildcard} [protocol-specific options] [log]
    Lab-A(config)#access-list 101 deny tcp 192.5.5.0 0.0.0.255 210.93.105.0 0.0.0.255 eq telnet log
  Group the ACL to one or more interfaces in interface configuration mode
  Router(config-if)#{protocol} access-group
  access-list-number {in/out}
    Lab-A(config-if)#ip access-group 101 out

## Slide 49: The Extended Parameters
  access-list-number
    choose from the range 100 to 199
  {protocol | protocol-number}
    For the CCNA, you only need to know ip and tcp--many more are available
  {source source-wildcard}
    same as in standard
  {destination destination-wildcard}
    formatted like the standard, but specifies the destination
  [protocol-specific options]
    This parameter is used to specify particular parts of a protocol that needs filtering.

## Slide 50: Port Numbers
Review the various port numbers for the tcp and udp protocols and know the most common ones below.
You can also simply type the name (telnet) instead of the number (23) in the {protocol-specific options}
Port Number | Description
21 | FTP
23 | Telnet
25 | SMTP
53 | DNS
69 | TFTP

## Slide 51: Correct Placement of Extended ACLs
In the graphic below, we want to deny network 221.23.123.0 from accessing the server 198.150.13.34.
What router and interface should the access list be applied to?
  Write the access list on Router C, apply it to the E0, and specify in
  This will keep the network free of traffic from 221.23.123.0 destined for 198.150.13.34 but still allow 221.23.123.0 access to the Internet

## Slide 52: Correct Placement of Extended ACLs
  Since extended ACLs have destination information, you want to place it as close to the source as possible.

## Slide 53: Writing & Applying the ACL
  Router-C(config)#access-list 100 deny ip 221.23.123.0 0.0.0.255 198.150.13.34 0.0.0.0
  Router-C(config)#access-list 100 permit ip any any
  Router-C(config)#int e0
  Router-C(config-if)#ip access-group 100 in

## Slide 54: Naming ACLs
One nice feature in the Cisco IOS is the ability to name ACLs. This is especially helpful if you need more than 99 standard ACLs on the same router.
Once you name an ACL, the prompt changes and you no longer have to enter the access-list and access-list-number parameters.
In the example below, the ACL is named over_and as a hint to how it should be placed on the interface--out
Lab-A(config)# ip access-list standard over_and
Lab-A(config-std-nacl)#deny host 192.5.5.10
.........
Lab-A(config-if)#ip access-group over_and out

## Slide 55: Verifying ACLs
Show commands:
  show access-lists
    shows all access-lists configured on the router
  show access-lists {name | number}
    shows the identified access list
  show ip interface
    shows the access-lists applied to the interface--both inbound and outbound.
  show running-config
    shows all access lists and what interfaces they are applied on

## Slide 56
谢 谢！